## Slide 1: Contingency table analyses
Miloš Radić 12/0010

## Slide 2: Introduction
Statistics in computing
  Huge amounts of data
  Substantial number of operations required
  Potentially highly parallel
Maxeler can give a significant speed-up!

## Slide 3: Contingency Table Analysis of two Distributions
Measurement of association for two variables
  Each sample has two variables we observe
  We are given a contingency table for those two
  We are interested in their relation to each other
Variable A
Variable B
Number of samples with a specific
value of A and B

## Slide 4: Contingency Table Analysis of two Distributions
Let’s use the Chi-square test
We need all the row and column sums
  This part of the algorithm is good for Maxeler
Scalar computations - CPU

## Slide 5: Sum of elements
Standard C implementation
  Initialize the sums with zeroes
  Use two nested for loops to sum
Naive Maxeler implementation
  Straightforward copy of C code to Maxeler
  Scheduling fails!

## Slide 6: Sum of elements
We have an issue when summing rows
Every tick we need the sum from the last tick
But addition has a delay of 12 ticks

## Slide 7: Sum of elements
MUX
ADD
INPUT
Result after 12 ticks
Input every tick
Compile error

## Slide 8: Sum of elements
Simple solution – use Autoloop Offset
Next input only when the last sum is computed
Bad performance, pipeline is stalled frequently

## Slide 9: Sum of elements
MUX
ADD
INPUT
Input every 12 ticks
-offset
Result after 12 ticks
Counter
=
offset - 1

## Slide 10: Sum of elements
Smarter solution – input transposition
We sum the colons using the original matrix
We sum the rows using the transposed matrix

## Slide 11: Sum of elements
MUX
ADD
ORIGINAL INPUT
-NUM_ROW
MUX
ADD
TRANSPOSED INPUT
-NUM_COL
COLON SUM
ROW SUM

## Slide 12: CONCLUSION
Idea of matrix transposition
In this particular example no speed-up benefit
  What it reveals is suggestive
  but what it conceals is vital (same as a bikini)
With more operations speed-up increases

## Slide 13: References
Trifunovic, N., Milutinovic, V., Salom, J., Kos,A., "Paradigm Shift in Big Data SuperComputing: DataFlow vs ControlFlow," Journal of Big Data, 2015, 2:4 (10 May 2015).
Milutinovic, V., Salom, J., Trifunovic, N., Giorgi, R., "Guide to DataFlow SuperComputing," Springer, 2015.

## Slide 14: Q&A