## Slide 1
Ognjen Šćekić
<number>/103
Altera vs. Xilinx
Ognjen Šćekić
ogi@cg.yu
prof. dr Veljko Milutinović
vm@etf.bg.ac.yu

## Slide 2: Clock Management
Ognjen Šćekić
<number>/103
All parts of a digital circuit need to be synchronized to a desired clock signal.
If a circuit is large, complex, and operating at high frequencies
the clock propagation delay and clock skew have a great impact on performance.
Therefore, providing a clock signal with zero-delay in all parts of an FPGA
becomes crucial.
The solution is to divide FPGA into regions that can work at different frequencies,
called clock domains.
Clock management comprises two basic functions:
  • remove clock skew and propagation delay
  • generate new clock signals with different frequencies and/or phases

## Slide 3: Removing Clock Skew
Ognjen Šćekić
<number>/103
It can be done using:
    DLLs – Delay-Locked Loops (Xilinx)
    PLLs – Phase-Locked Loops (Altera)
Figure 3a - DLL block diagram
Figure 3b - PLL block diagram
They both compensate for the delay generated on the routing network inside the FPGA, providing zero-delay clock signal to different parts of FPGA.

## Slide 4: Delay-Locked Loop
Ognjen Šćekić
<number>/103
Delay-line produces a delayed version of the input clock CLKIN.
Clock distribution network routes the clock to FPGA interior
and to the feedback CLKFB pin.
Control logic sample the input clock and the feedback clock
in order to adjust the delay line.
Delay-line consists on an array of delay elements,
typically CMOS voltage-controlled inverters connected in series.
DLL works by inserting delay between the input clock and the feedback clock until the two rising edges align,
putting the two clocks in phase.
When the two clocks are in phase, the DLL "locks".
Thus, the DLL output clock compensates for the delay
in the clock distribution network.

## Slide 5: Phase-Locked Loop
Ognjen Šćekić
<number>/103
Instead of a delay line, the PLL uses a voltage controlled oscillator
which generates a clock signal that approximates the input clock CLKIN.
Control logic, consisting of a phase detector and filter,
adjusts the oscillator frequency and phase to compensate for the clock distribution delay.
When the clocks are aligned the PLL "locks".

## Slide 6: PLL vs. DLL
Ognjen Šćekić
<number>/103
PLL DLL
Advantage:
does not accumulate phase error
Drawback:
oscillator accumulates phase error
Advantage:
frequency synthesis is easier
because of oscillator
Drawback:
frequency synthesis is more difficult
Altera uses PLLs and Xilinx uses DLLs.

## Slide 7: Clock Generation & Phase Shifting
Ognjen Šćekić
<number>/103
Beside clock skew elimination, DLLs (PLLs) are also used for:
Clock managers need to be resistant to temperature/voltage variations.
frequency multiplication and division
duty-cycle regulation
phase shifting
Clock manipulation dramatically simplifies the design
and improves performance.
At the same time it provides many design alternatives.

## Slide 8: Embedded Memory
Ognjen Šćekić
<number>/103
Using LUTs as registers does not provide enough space or versatility.
Time-dependent applications, performing many computations,
need an entire built-in memory.
The main advantages of embedded (built-in) memory are:
short access time
high bandwidth
great versatility
It can behave like:
RAM
ROM
Buffer (FIFO, LIFO, etc.)
Cache
Shift registers
etc…

## Slide 9: DSP Capabilities
Ognjen Šćekić
<number>/103
DSP – Digital Signal Processing
Majority of FPGA applications require some sort of DSP.
In order to increase efficiency DSP computations are executed in parallel - pipelining.
Special DSP units have been developed to fully exploit FPGA's adaptable structure.
These units are designed to optimize execution of commonly used DSP algorithms:
filtering, encoding/decoding, equalization, modulation, FFT, etc
They usually contain:
multipliers (in parallel), accumulators, adders and shift registers

## Slide 10: Embedded Memory
Ognjen Šćekić
<number>/103
Consists of columns of M4K memory blocks:

## Slide 11: Embedded Memory (2)
Ognjen Šćekić
<number>/103
The M4K blocks support the following features:
4,608 RAM bits (4Kbits + parity bits – one for each byte)
250-MHz performance
True dual-port memory
Supports any combination of two-port operations: 2 reads, 2 writes, or 1 read and 1 write at different clock frequencies.
Simple dual-port memory
Simultaneous reads and writes are supported.
Single-port memory
Simultaneous reads and writes are not allowed.
Shift register

## Slide 12: Embedded Memory (3)
Ognjen Šćekić
<number>/103
The M4K blocks support the following features:
FIFO buffer
ROM
When configured as RAM or ROM, you can use an initialization file to preload the memory contents.
Byte enable
Allows the input data to be masked so the device can write to specific bytes. The unwritten bytes retain the previous written value.
Address clock enable
Used to hold the previous address value for as long as the signal is enabled. This feature is useful in handling cache misses.
Content Addressable memory (CAM)  Associative memory

## Slide 13: Embedded Multipliers
Ognjen Šćekić
<number>/103
Located in columns high as one LAB row:

## Slide 14: Embedded Multipliers (2)
Ognjen Šćekić
<number>/103
Multiplier blocks are optimized for intensive Digital Signal Processing functions, such as:
finite impulse response (FIR) filters, Fast Fourier Transform (FFT), Discrete Cosine Transform (DCT) functions, etc.
Operate at up to 250 MHz.
Embedded multipliers can work in 2 basic operational modes:
  One 18b x 18b multiplier
  Two independent 9b x 9b multipliers

## Slide 15: Embedded Multipliers (3)
Ognjen Šćekić
<number>/103
The embedded multiplier consists of the following elements:
    Multiplier block
    Input and output registers
    Input and output interfaces
These signals control operand representation:
signed or unsigned
Input Register (used optionally)
Output Register (used optionally)