## Slide 1: Spherical Code Construction
Vojin Šenk (vojin_senk@uns.ac.rs)
Ivan Stanojević (cet_ivan@uns.ac.rs)
Mladen Kovačević (kmladen@uns.ac.rs)
University of Novi Sad

## Slide 2: Problem Formulation
Given the dimension, D, and the number of points, N, find vectors
r1,r2,...,rN,
on the unit sphere,
|rn|=((rn(1))2+(rn(2))2+...+ (rn(D))2)1/2=1,
such that their minimum distance,
dmin=minn≠m|rn - rm|,
is maximized.

## Slide 3: Variable Repulsion Force Method
Algorithm overview:
  Randomly select initial vectors.
  Iteratively move every vector in the direction of the repulsion force of other vectors, constraining it to the unit sphere.
  Change the dependence of the force on the distance, such that closer vectors have greater influence and repeat.

## Slide 4: Variable Repulsion Force Method
Initial vector coordinates are chosen according to the normal distribution
r'n(d):N(0,1),
and vectors are then projected on the unit sphere
rn=r'n/|r'n|.
No directions are privileged.

## Slide 5: Variable Repulsion Force Method
Force from other vectors is calculated according to the inverse power law of the distance
F'n=∑m≠n (rn-rm)/|rn-rm|β.
To avoid numerical difficulties, the force is normalized
Fn=F'n/|F'n|.

## Slide 6: Variable Repulsion Force Method
The point is moved in the direction of the normalized force and projected on the unit sphere,
r'n=rn+tnFn,
rn:=r'n/|r'n|,
where
tn=δn/(2β),
and
δn=minm≠n|rn - rm|2.

## Slide 7: Variable Repulsion Force Method
Since the force is being normalized, it can be scaled before that. A convenient way to do it is
F'n=∑m≠n(δn/|rn - rm|2)β/2(rn - rm),
since squared distances are easier to calculate, and the expression in the first pair of parentheses is always ≤1.
As β→∞, the closest points have the greatest influence, and the minimum distance is maximized.

## Slide 8: Variable Repulsion Force Method
Overview of steps for a single vector:
  1. δn=minm≠n|rn - rm|2
  2. F'n=∑m≠n(δn/|rn - rm|2)β/2(rn - rm)
  3. Fn=F'n/|F'n|
  4. r'n=rn+(δn/(2β))Fn
  5. rn:=r'n/|r'n|

## Slide 9: Implementation Architecture
dataflow engine
floating point
floating point
fixed point
fixed point
host
S/P and type conversion
vector update
P/S and type conversion

## Slide 10: Vector Operations
+
+
+
Addition (Subtraction)

## Slide 11: Vector Operations
Multiplication by a scalar
×
×
×

## Slide 12: Vector Operations
(Squared) Norm calculation
2
2
2
+
√

## Slide 13: High Level Pipeline
While rn is being calculated, δn+1 can be calculated at the same time.
δ1
r1 δ2
r2 δ3
r3 δ4
... ...
rN-1 δN
rN
Total time = N(N+1) cycles.
time

## Slide 14: Vector Update
δ
F,r'

## Slide 15: Implementation Considerations
Maximum dimension of vectors, Dmax, and their maximum number, Nmax, must be hardcoded in the dataflow structure.
After fine tuning for MAX2, Dmax=6, Nmax=16384, with real numbers as signed fixed point [3].[44] (bits).
N and D for a particular problem instance are given as scalar inputs.

## Slide 16: Results

## Slide 17: Execution Times

## Slide 18: Power Consumption
Operation Mode | Power [W]
Idle | 68
Software only execution | 88
Hardware accelerated execution | 74
CPU = Intel i7-3770K@3.5GHz.
All measurements are performed on the host mains cable.
Relative additional power savings:
(88-68)/(74-68)=3.33×

## Slide 19: Conclusion
Asymptotic acceleration = (18÷24)× .
More powerful hardware (e.g., MAX3) would enable higher Dmax and Nmax and higher speed.
Changing the dataflow structure (e.g., to do vector operations serially) could also enable higher Dmax and Nmax at the cost of lower speed.

## Slide 20: Q&A: cet_ivan@uns.ac.rs