## Slide 1: DataFlow Computing for Exascale HPC
Veljko Milutinović and Saša Stojanović
University of Belgrade
Oliver Pell and Oskar Mencer
Maxeler Technologies

## Slide 2: Essence of the Approach!
Compiling below the machine code level brings speedups;
also a smaller power, size, and cost.
The price to pay:
The machine is more difficult to program.
Consequently:
Ideal for WORM applications :)
Examples:
GeoPhysics, banking, life sciencies, datamining...

## Slide 3: ControlFlow vs. DataFlow

## Slide 4: DataFlow Programming

## Slide 5: The essential figure
Assumptions:
1. Software includes enough parallelism to keep all cores busy
2. The only limiting factor is the number of cores.
tGPU =
N * NOPS * CGPU*TclkGPU / NcoresGPU
tCPU =
N * NOPS * CCPU*TclkCPU /NcoresCPU
tDF = NOPS * CDF * TclkDF +
(N – 1) * TclkDF / NDF

## Slide 6: MultiCore
DualCore?
Where are the horses going?

## Slide 7: ManyCore
Is it possible to use 2000 chicken instead of two horses?
?
==

## Slide 8: ManyCore
2 x 1000 chickens

## Slide 9: DataFlow
How about 2 000 000 ants?
Data

## Slide 10: DataFlow
Marmalade
Big Data Input
Results

## Slide 11: Why is DataFlow so Much Faster?
Factor: 20 to 200
MultiCore/ManyCore
Dataflow
Machine Level Code
Gate Transfer Level

## Slide 12: Why are Electricity Bills so Small?
Factor: 20
MultiCore/ManyCore
Dataflow

## Slide 13: Why is the Cubic Foot so Small?
Factor: 20
Data Processing
Process Control
Data Processing
Process Control
MultiCore/ManyCore
Dataflow

## Slide 14: Required Programming Effort?
MultiCore:
  Explain what to do, to the driver
  Caches, instruction buffers, and predictors needed
ManyCore:
  Explain what to do, to many sub-drivers
  Reduced caches and instruction buffers needed
DataFlow:
  Make a field of processing gates
  No caches, instruction buffers, or predictors needed

## Slide 15: Required Debug Effort?
MultiCore:
  Business as usual
ManyCore:
  More difficult
DataFlow:
  Much more difficult
  Debugging both, application and configuration code

## Slide 16: Required Compilation Effort?
MultiCore/ManyCore:
  Several minutes
DataFlow:
  Several hours

## Slide 17: Now the Fun Part

## Slide 18: Required Space?
MultiCore:
  Horse stable
ManyCore:
  Chicken house
DataFlow:
  Ant hole

## Slide 19: Required Energy?
MultiCore:
  Haystack
ManyCore:
  Cornbits
DataFlow:
  Crumbs

## Slide 20: Why Faster?
Small Data

## Slide 21: Why Faster?
Medium Data

## Slide 22: Why Faster?
Big Data

## Slide 23: DataFlow for Exascale Challenges
Power consumption
  Massive static parallelism at low clock frequencies
Concurrency and communication
  Concurrency between millions of tiny cores difficult, “jitter” between cores will harm performance at synchronization points.
  “Fat” dataflow chips minimize number of engines needed and statically scheduled dataflow cores minimize jitter.
Reliability and fault tolerance
  10-100x fewer nodes, failures much less often
Memory bandwidth and FLOP/byte ratio
  Optimize data movement first, and computation second.

## Slide 24: Combining ControlFlow with DataFlow
DataFlow engines handle the bulk part of computation (as a “coprocessor”)
Traditional ControlFlow CPUs run OS, main application code etc
Lots of different ways these can be combined

## Slide 25: Maxeler Hardware
CPUs plus DFEs Intel Xeon CPU cores and up to 4 DFEs with 192GB of RAM
DFEs shared over Infiniband
Up to 8 DFEs with 384GB of RAM and dynamic allocation of DFEs to CPU servers
Low latency connectivity
Intel Xeon CPUs and 1-2 DFEs with up to six 10Gbit Ethernet connections
MaxWorkstation
Desktop development system
MaxCloud
On-demand scalable accelerated compute resource, hosted in London

## Slide 26: MPC-C
Tightly coupled DFEs and CPUs
Simple data center architecture with identical nodes

## Slide 27: Credit Derivatives Valuation & Risk
Compute value of complex financial derivatives (CDOs)
Typically run overnight, but beneficial to compute in real-time
Many independent jobs
Speedup: 220-270x
Power consumption per node drops from 250W to 235W/node
O. Mencer and S. Weston, 2010

## Slide 28: CRS Trace Stacking
Seismic processing application
Velocity independent / data driven method to obtain a stack of traces, based on 8 parameters
  Search for every sample of each output trace
P. Marchetti et al, 2010
2 parameters ( emergence angle & azimuth )
3 Normal Wave front parameters ( KN,11; KN,12 ; KN22 )
3 NIP Wave front parameters ( KNip,11; KNip,12 ; KNip22 )

## Slide 29: CRS Results
Performance of MAX2 DFEs vs. 1 CPU core
  Land case (8 params), speedup of 230x
  Marine case (6 params), speedup of 190x
CPU Coherency
MAX2 Coherency

## Slide 30: MPC-X
DFEs are shared resources on the cluster, accessible via Infiniband connections
Loose coupling optimizes efficiency
Communication managed in hardware for performance

## Slide 31: Major Classes of Applications
Coarse grained, stateful
  CPU requires DFE for minutes or hours
Fine grained, stateless transactional
  CPU requires DFE for ms to s
  Many short computations
Fine grained, transactional with shared database
  CPU utilizes DFE for ms to s
  Many short computations, accessing common database data

## Slide 32: Coarse Grained: FD Wave Modeling
Long runtime, but:
Memory requirements change dramatically based on modelled frequency
Number of DFEs allocated to a CPU process can be easily varied to increase available memory
Streaming compression
Boundary data exchanged over chassis MaxRing

## Slide 33: Fine Grained, Stateless: BSOP
Portfolio with thousands of Vanilla European Options
Analyse > 1,000,000 scenarios
Many CPU processes run on many DFEs
  Each transaction executes on any DFE in the assigned group atomically
~50x MPC-X vs. multi-core x86 node
CPU
DFE
Loop over instruments
Random number generator and sampling of underliers
Price instruments using Black Scholes
Tail analysis on CPU
CPU
DFE
Loop over instruments
Random number generator and sampling of underliers
Price instruments using Black Scholes
Tail analysis on CPU
CPU
DFE
Loop over instruments
Random number generator and sampling of underliers
Price instruments using Black Scholes
Tail analysis on CPU
CPU
DFE
Loop over instruments
Random number generator and sampling of underliers
Price instruments using Black Scholes
Tail analysis on CPU
DFE
Loop over instruments
CPU
Market and instruments
data
Random number generator and sampling of underliers
Price instruments using Black Scholes
Instrument values
Tail analysis on CPU
Notes: Elastic makes things worse

## Slide 34: Fine Grained, Shared Data: Searching
DFE DRAM contains the database to be searched
CPUs issue transactions find(x, db)
Complex search function
  Text search against documents
  Shortest distance to coordinate (multi-dimensional)
  Smith Waterman sequence alignment for genomes
Any CPU runs on any DFE that has been loaded with the database
  MaxelerOS may add or remove DFEs from the processing group to balance system demands
  New DFEs must be loaded with the search DB before use

## Slide 35: Conclusion
Dataflow computing focuses on data movement and utilizes massive parallelism at low clock frequencies
Improved performance, power efficiency, system size, and data movement can help address exascale challenges
Mix of DataFlow with ControlFlow and interconnect can be balanced at a system level
What’s next?

## Slide 36
The TriPeak
BSC + Maxeler

## Slide 37: The TriPeak
MontBlanc = A ManyCore (NVidia) + a MultiCore (ARM)
Maxeler = A FineGrain DataFlow (FPGA)
How about a happy marriage
of MontBlanc and Maxeler?
In each happy marriage,
it is known who does what :)

## Slide 38: Core of the Symbiotic Success:
An intelligent scheduler,
partially implemented for compile time,
and partially for run time.
At compile time:
Checking what part of code fits where
(MontBllanc or Maxeler).
At run time:
Rechecking the compile time decision,
based on the current data values

## Slide 39
39

## Slide 40
© H. Maurer
40

## Slide 41
© H. Maurer
41

## Slide 42
© H. Maurer
42
vm@etf.rs
Q&A
oliver@maxeler.com