## Slide 1: Selected MaxCompiler Examples
Sasa Stojanovic
stojsasa@etf.rs
Veljko Milutinovic
vm@etf.rs

## Slide 2: How-to? What-to?
One has to know how to program DataFlow machines, in order to get the best possible speedup out of them!
For some applications (G), there is a large difference between what an experienced programmer achieves, and what an un-experienced one can achieve!
For some other applications (B), no matter how experienced the programmer is, the speedup will not be revolutionary (may be even <1).
Introduction

## Slide 3: Lemas
Lemas:
  1. The how-to and how-not-to is important to know!
  2. The what-to and what-not-to is important to know!
N.B.
  The how-to is taught through most of the examples to follow (all except the introductory ones).
  The what-to/what-not-to is taught using a figure.
Introduction

## Slide 4: The Essential Figure:
Introduction
Assumptions:
1. Software includes enough parallelism to keep all cores busy
2. The only limiting factor is the number of cores.
tCPU = N * NOPS * CCPU*TclkCPU /NcoresCPU
tDF = NOPS * CDF * TclkDF + (N – 1) * TclkDF / NDF

## Slide 5: Bottomline:
When is DataFlow better?
  If the number of operations in a single loop iteration is above some critical value
  Then More data items means more advantage for DataFlow.
In other words:
  More data does not mean better performance if the #operations/iteration is below a critical value.
Conclusion:
  If we see an application with a small #operations/iteration, it is possibly (not always) a “what-not-to” application, and we better execute it on the host; otherwise, we will (or may) have a slowdown.
Introduction
ADDITIVE SPEEDUP ENABLER
ADDITIVE SPEEDUP MAKER

## Slide 6: To have it more concrete:
DataFlow: One new result in each cycle e.g. Clock = 100MHz Period = 10ns One result every 10ns [No matter how many operations in each loop iteration] Consequently: More operations does not mean proportionally more time; however, more operations means higher latency till the first result.
MultiCore: One new result after each iteration e.g. Clock=4GHz Period = 250ps One result every 250ps times #ops [If #ops > 40 => DataFlow is better, although it uses a slower clock]
Also: The MltiCore example will feature an additional slowdown, due to memory hierarchy access and pipeline related hazards => critical #ops (bringing the same performance) is significantly below 40!!!
Introduction

## Slide 7: Don’t missunderstand!
DataFlow has no cache, but does have a memory hierarchy.
However, memory hierarchy access with DataFlow is carefully planed by the programmer at the program write time
As opposed to memory hierarchy access with a MultiCore which calculates the access address at the program run time.
Introduction

## Slide 8: N.B.
Java to configure Maxeler DataFlow! C to program the host!
One or more kernels! Only one manager!
In theory, Simulator builder not needed if a card is used. In practice, you need it until the testing is over, since the compilation process is slow, for hardware, and fast, for software (simulator).
Introduction

## Slide 9: Example No.1: Hello World!
Write a program that sends the “Hello World!” string to the MAX2 card, for the MAX2 card kernel to return it back to the host.
To be learned through this example:
  How to make the configuration of the accelerator (MAX2 card) using Java:
    How to make a simple kernel (ops description) using Java (the only language),
    How to write the standard manager (config description based on kernel(s)) using Java,
  How to test the kernel using a test (code+data) written in Java,
  How to compile the Java code for MAX2,
  How to write a simple C code that runs on the host and triggers the kernel,
    How to write the C code that streams data to the kernel,
    How to write the C code that accepts data from the kernel,
  How to simulate and execute an application program in C that runs on the host and periodically calls the accelerator.
Example No. 1

## Slide 10: Standard Files in a MAX Project
One or more kernel files, to define operations of the application:
  <app_name>Kernel[<additional_name>].java
One (or more) Java file, for simulation of the kernel(s):
  <app_name>SimRunner.java
One manager file for transforming the kernel(s) into the configuration of the MAX card (instantiation and connection of kernels):
  <app_name>Manager.java
Simulator builder:
  <app_name>HostSimBuilder.java
Hardware builder:
  <app_name>HWBuilder.java
Application code that uses the MAX card accelerator:
  <app_name>HostCode.c
Makefile
  A script file that defines the compilation related commands
Example No. 1

## Slide 11: example1Kernel.java
package ind.z1;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.kernelcompiler.KernelParameters;
import com.maxeler.maxcompiler.v1.kernelcompiler.types.base.HWVar;
public class helloKernel extends Kernel {
public helloKernel(KernelParameters parameters) {
super(parameters);
// Input:
HWVar x = io.input("x", hwInt(8));
HWVar result = x;
// Output:
io.output("z", result, hwInt(8));
}
}
Example No. 1
It is possible to substitute the last three lines with:
io.output("z", x, hwInt(8));

## Slide 12: example1SimRunner.java
package ind.z1;
import com.maxeler.maxcompiler.v1.managers.standard.SimulationManager;
public class helloSimRunner {
public static void main(String[] args) {
SimulationManager m = new SimulationManager(“helloSim");
helloKernel k = new helloKernel( m.makeKernelParameters() );
m.setKernel(k);
m.setInputData("x", 1, 2, 3, 4, 5, 6, 7, 8);
m.setKernelCycles(8);
m.runTest();
m.dumpOutput();
double expectedOutput[] = { 1, 2, 3, 4, 5, 6, 7, 8 };
m.checkOutputData("z", expectedOutput);
m.logMsg("Test passed OK!");
}
}
Example No. 1

## Slide 13: example1HostSimBuilder.java
package ind.z1;
import static config.BoardModel.BOARDMODEL;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.managers.standard.Manager;
import com.maxeler.maxcompiler.v1.managers.standard.Manager.IOType;
public class helloHostSimBuilder {
public static void main(String[] args) {
Manager m = new Manager(true,”helloHostSim", BOARDMODEL);
Kernel k = new
helloKernel(m.makeKernelParameters(“helloKernel"));
m.setKernel(k);
m.setIO(IOType.ALL_PCIE);
m.build();
}
}
Example No. 1

## Slide 14: example1HwBuilder.java
package ind.z1;
import static config.BoardModel.BOARDMODEL;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.managers.standard.Manager;
import com.maxeler.maxcompiler.v1.managers.standard.Manager.IOType;
public class helloHWBuilder {
public static void main(String[] args) {
Manager m = new Manager(“hello", BOARDMODEL);
Kernel k = new helloKernel( m.makeKernelParameters() );
m.setKernel(k);
m.setIO(IOType.ALL_PCIE);
m.build();
}
}
Example No. 1

## Slide 15: example1HostCode.c 1/2
#include <stdio.h>
#include <MaxCompilerRT.h>
int main(int argc, char* argv[])
{
char *device_name = (argc==2 ? argv[1] : "/dev/maxeler0");
max_maxfile_t* maxfile;
max_device_handle_t* device;
char data_in1[16] = "Hello world!";
char data_out[16];
printf("Opening and configuring FPGA.\n");
maxfile = max_maxfile_init_hello();
device = max_open_device(maxfile, device_name);
max_set_terminate_on_error(device);
Example No. 1

## Slide 16: example1HostCode.c 2/2
printf("Streaming data to/from FPGA...\n");
max_run(device,
max_input("x", data_in1, 16 * sizeof(char)),
max_output("z", data_out, 16 * sizeof(char)),
max_runfor(“helloKernel", 16),
max_end());
printf("Checking data read from FPGA.\n");
max_close_device(device);
max_destroy(maxfile);
return 0;
}
Example No. 1

## Slide 17: Makefile
# Root of the project directory tree
BASEDIR=../../..
# Java package name
PACKAGE=ind/z1
# Application name
APP=example1
# Names of your maxfiles
HWMAXFILE=$(APP).max
HOSTSIMMAXFILE=$(APP)HostSim.max
# Java application builders
HWBUILDER=$(APP)HWBuilder.java
HOSTSIMBUILDER=$(APP)HostSimBuilder.java
SIMRUNNER=$(APP)SimRunner.java
# C host code
HOSTCODE=$(APP)HostCode.c
# Target board
BOARD_MODEL=23312
# Include the master makefile.include
nullstring :=
space := $(nullstring) # comment
MAXCOMPILERDIR_QUOTE:=$(subst $(space),\ ,$(MAXCOMPILERDIR))
include $(MAXCOMPILERDIR_QUOTE)/examples/common/Makefile.include
Example No. 1

## Slide 18: BoardModel.java
package config;
import com.maxeler.maxcompiler.v1.managers.MAX2BoardModel;
public class BoardModel {
public static final MAX2BoardModel BOARDMODEL = MAX2BoardModel.MAX2336B;
}
Example No. 1

## Slide 19: Example No. 2: Vector Addition
Write a program that adds two arrays of floating point numbers.
Program reads the size of arrays, makes two arrays with an arbitrary content (test inputs), and adds them using a MAX card.
Example No. 2

## Slide 20: example2Kernel.Java
package ind.z2;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.kernelcompiler.KernelParameters;
import com.maxeler.maxcompiler.v1.kernelcompiler.types.base.HWVar;
public class example2Kernel extends Kernel {
public example2Kernel(KernelParameters parameters) {
super(parameters);
// Input
HWVar x = io.input("x", hwFloat(8,24));
HWVar y = io.input("y", hwFloat(8,24));
HWVar result = x + y;
// Output
io.output("z", result, hwFloat(8,24));
}
}
Example No. 2

## Slide 21: example2SimRunner.java
package ind.z2;
import com.maxeler.maxcompiler.v1.managers.standard.SimulationManager;
public class example2SimRunner {
public static void main(String[] args) {
SimulationManager m = new SimulationManager("example2Sim");
example2Kernel k = new example2Kernel( m.makeKernelParameters() );
m.setKernel(k);
m.setInputData("x", 1, 2, 3, 4, 5, 6, 7, 8);
m.setInputData("y", 2, 3, 4, 5, 6, 7, 8, 9);
m.setKernelCycles(8);
m.runTest();
m.dumpOutput();
double expectedOutput[] = { 3, 5, 7, 9, 11, 13, 15, 17 };
m.checkOutputData("z", expectedOutput);
m.logMsg("Test passed OK!");
}
}
Example No. 2

## Slide 22: example2HostSimBuilder.java
package ind.z2;
import static config.BoardModel.BOARDMODEL;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.managers.standard.Manager;
import com.maxeler.maxcompiler.v1.managers.standard.Manager.IOType;
public class example2HostSimBuilder {
public static void main(String[] args) {
Manager m = new Manager(true,"example2HostSim", BOARDMODEL);
Kernel k = new example2Kernel( m.makeKernelParameters("example2Kernel") );
m.setKernel(k);
m.setIO(IOType.ALL_PCIE);
m.build();
}
}
Example No. 2

## Slide 23: example2HWBuilder.java
package ind.z2;
import static config.BoardModel.BOARDMODEL;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.managers.standard.Manager;
import com.maxeler.maxcompiler.v1.managers.standard.Manager.IOType;
public class example2HWBuilder {
public static void main(String[] args) {
Manager m = new Manager("example2", BOARDMODEL);
Kernel k = new example2Kernel( m.makeKernelParameters() );
m.setKernel(k);
m.setIO(IOType.ALL_PCIE);
m.build();
}
}
Example No. 2

## Slide 24: example2HostCode.c 1/2
#include <stdio.h>
#include <stdlib.h>
#include <MaxCompilerRT.h>
int main(int argc, char* argv[])
{
char *device_name = (argc==2 ? argv[1] : "/dev/maxeler0");
max_maxfile_t* maxfile;
max_device_handle_t* device;
float *data_in1, *data_in2, *data_out;
unsigned long N, i;
printf("Enter size of array: "); scanf("%lu",&N);
data_in1 = malloc(N * sizeof(float));
data_in2 = malloc(N * sizeof(float));
data_out = malloc(N * sizeof(float));
for(i = 0; i < N; i++){
data_in1[i] = i%10;
data_in2[i] = i%3;
}
printf("Opening and configuring FPGA.\n");
Example No. 2

## Slide 25: example2HostCode.c 2/2
maxfile = max_maxfile_init_example2();
device = max_open_device(maxfile, device_name);
max_set_terminate_on_error(device);
printf("Streaming data to/from FPGA...\n");
max_run(device,
max_input("x", data_in1, N * sizeof(float)),
max_input("y", data_in2, N * sizeof(float)),
max_output("z", data_out, N * sizeof(float)),
max_runfor("example2Kernel", N),
max_end());
printf("Checking data read from FPGA.\n");
for(i = 0; i < N; i++)
if (data_out[i] != i%10 + i%3){
printf("Error on element %d. Expected %f, but found %f.", i, (float)(i%10+i%3), data_out[i]);
break;
}
max_close_device(device);
max_destroy(maxfile);
return 0;
}
Example No. 2

## Slide 26: Example No. 3: Optimized Array Summation
Write an optimized program that calculates the sum of numbers in an input array
First, calculate several parallel/partial sums; then, add them at the end
Example No. 3

## Slide 27: example3Kernel1.java
package ind.z3;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.kernelcompiler.KernelParameters;
import com.maxeler.maxcompiler.v1.kernelcompiler.types.base.HWVar;
import com.maxeler.maxcompiler.v1.kernelcompiler.types.base.HWType;
public class example30Kernel1 extends Kernel {
public example3Kernel1(KernelParameters parameters) {
super(parameters);
final HWType scalarType = hwFloat(8,24);
HWVar cnt = control.count.simpleCounter(64);
// Input
HWVar N = io.scalarInput("N", hwUInt(64));
HWVar x = io.input("x", hwFloat(8,24) );
HWVar sum = scalarType.newInstance(this);
HWVar result = x + (cnt>0?sum:0.0);
sum <== stream.offset(result, -13);
// Output
io.output("z", result, hwFloat(8,24), cnt > N-14);
}
}
Example No. 3

## Slide 28: example3Kernel2.java
package ind.z3;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.kernelcompiler.KernelParameters;
import com.maxeler.maxcompiler.v1.kernelcompiler.types.base.HWVar;
import com.maxeler.maxcompiler.v1.kernelcompiler.types.base.HWType;
import com.maxeler.maxcompiler.v1.kernelcompiler.stdlib.core.CounterChain;
public class example3Kernel2 extends Kernel {
public example3Kernel2(KernelParameters parameters) {
super(parameters);
final HWType scalarType = hwFloat(8,24);
CounterChain cc = control.count.makeCounterChain();
HWVar cnt = cc.addCounter(14,1);
HWVar depth = cc.addCounter(13,1);
// Input
HWVar x = io.input("x", hwFloat(8,24), depth.eq(0) );
HWVar sum = scalarType.newInstance(this);
HWVar result = x + (cnt>0?sum:0.0);
sum <== stream.offset(result, -13);
// Output
io.output("z", result, hwFloat(8,24), cnt.eq(12));
}
}
Example No. 3

## Slide 29: example3SimRunner.java
package ind.z3;
import com.maxeler.maxcompiler.v1.managers.standard.SimulationManager;
public class example3SimRunner {
public static void main(String[] args) {
SimulationManager m = new SimulationManager("example3Sim");
example3Kernel1 k = new example3Kernel1( m.makeKernelParameters() );
m.setKernel(k);
m.setInputData("x", 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16, 17, 18, 19, 20, 21, 22, 23, 24, 25, 26);
m.setKernelCycles(26);
m.runTest();
m.dumpOutput();
double exOutput[] = { 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 15, 17, 19, 21, 23, 25, 27, 29, 31, 33, 35, 37, 39 };
m.checkOutputData("z", exOutput);
m.logMsg("Test passed OK!");
}
}
Example No. 3

## Slide 30: example3Manager.java
package ind.z3;
import com.maxeler.maxcompiler.v1.managers.custom.blocks.KernelBlock;
import com.maxeler.maxcompiler.v1.managers.custom.CustomManager;
import com.maxeler.maxcompiler.v1.managers.MAXBoardModel;
class example3Manager extends CustomManager {
public example3Manager(boolean is_simulation, String name, MAXBoardModel board_model ){
super(is_simulation, board_model, name);
KernelBlock kb1 = addKernel(new example10Kernel1(makeKernelParameters("example10Kernel1")));
KernelBlock kb2 = addKernel(new example10Kernel2(makeKernelParameters("example10Kernel2")));
kb1.getInput("x") <== addStreamFromHost("x");
kb2.getInput("x") <== kb1.getOutput("z");
addStreamToHost("z") <== kb2.getOutput("z");
}
}
Example No. 3

## Slide 31: example3HostSimBuilder.java
package ind.z3;
import static config.BoardModel.BOARDMODEL;
import com.maxeler.maxcompiler.v1.managers.BuildConfig;
import com.maxeler.maxcompiler.v1.managers.BuildConfig.Level;
public class example3HostSimBuilder {
public static void main(String[] args) {
example3Manager m = new example3Manager(true,"example3HostSim", BOARDMODEL);
m.setBuildConfig(new BuildConfig(Level.FULL_BUILD));
m.build();
}
}
Example No. 3

## Slide 32: example3HWBuilder.java
package ind.z3;
import static config.BoardModel.BOARDMODEL;
import com.maxeler.maxcompiler.v1.kernelcompiler.Kernel;
import com.maxeler.maxcompiler.v1.managers.standard.Manager;
import com.maxeler.maxcompiler.v1.managers.standard.Manager.IOType;
public class example3HWBuilder {
public static void main(String[] args) {
example3Manager m = new example3Manager(false,"example10HostSim", BOARDMODEL);
m.setBuildConfig(new BuildConfig(Level.FULL_BUILD));
m.build();
}
}
Example No. 10

## Slide 33: example3HostCode.c 1/2
#include <stdio.h>
#include <stdlib.h>
#include <MaxCompilerRT.h>
int main(int argc, char* argv[])
{
char *device_name = (argc==2 ? argv[1] : "/dev/maxeler0");
max_maxfile_t* maxfile;
max_device_handle_t* device;
float *data_in1, *data_out, expected = 0;
unsigned long N, i;
printf("Enter size of array (it will be truncated to the firs lower number dividable with 13): ");
scanf("%lu",&N);
N /= 13;
N *= 13;
data_in1 = malloc(N * sizeof(float));
data_out = malloc(1 * sizeof(float));
for(i = 0; i < N; i++){
data_in1[i] = i%10;
expected += data_in1[i];
}
Example No. 3

## Slide 34: example3HostCode.c 2/2
printf("Opening and configuring FPGA.\n");
maxfile = max_maxfile_init_example3();
device = max_open_device(maxfile, device_name);
max_set_terminate_on_error(device);
max_set_scalar_input_f(device, "example10Kernel1.N", N, FPGA_A);
max_upload_runtime_params(device, FPGA_A);
printf("Streaming data to/from FPGA...\n");
max_run(device,
max_input("x", data_in1, N * sizeof(float)),
max_output("z", data_out, 2 * sizeof(float)),
max_runfor("example3Kernel1", N),
max_runfor("example3Kernel2", 13*12+2),
max_end());
printf("Checking data read from FPGA.\n");
printf("Expected: %f, returned: %f\n", expected, *data_out);
max_close_device(device);
max_destroy(maxfile);
return 0;
}
Example No. 3

## Slide 35: Hvala na pažnji!
Saša Stojanović
stojsasa@etf.bg.ac.rs